## Slide 1
INTRODUCTION
To Telecommunications and Networking
An Instructor-led Course Designed Specifically for FDIC Risk Management Examiners

## Slide 2
Our Goal of this Week
Is to begin cracking this code
What are all these things? Which of them have I seen before?
  Which do I use myself, and how, and for what?
Why switches, routers, firewalls, modems, and other boxes?
  What do they do, and how do they work?
  What standards govern their behavior and operation?
What’s in the cloud-things, and lines that show connections?
  Are all the connections alike or equivalent?
What is safe and what is not?
Where are the risks? There is always some risk!
What questions can I ask to learn about a bank’s network?
  How can I know if my banks are using best practices?
Is the banking industry taking advantage of available value?

## Slide 3: Overall Goals of this Course
Understand the fundamental role of networks in banks
Explore the technical aspects of voice and data networks
Learn the common network technologies used in banks
Expand and define common acronyms and terminology
Discuss current trends in telecommunications and networking
Raise your comfort level with telecommunications and networking in conversations bank IT staff
Sharpen your wits regarding bank IT exams
Discover risk and what can be done about it
Learn where bank networking may be in a few years

## Slide 4: Introductions
We have ~4.5 days together this week! I’ll go first:
My name is Matt Kolon, I’m a Senior MTS at Hill Associates
  I’m a long-time networking, bank IT, and telecom geek.
  I’ve worked for Cisco, Juniper, and Brocade as well as Hill Associates
  From 2005 to 2017 I lived in 香港, 北京, and 東京.
  Now I live in Underhill, Vermont where I ski and ride my bikes a lot.
  I feel banking is completely dependent on IT and telecommunications.
  This week I’d like us to find places where risk is hiding in bank networks.
Please tell us about you!
  Where do you live and work?
  What’s your role?
  What do you do for fun?
  What would you like to take away from this course?

## Slide 5: Agenda
Introduction to data networks and the telecom industry
Communication models (OSI RM, the Internet protocol suite, and the modern five-layer telecom model)
How data and voice networks work
What all those boxes do!
The big topics in the operation of the internet
Network security from the inside and outside
Applying our knowledge to bank networks
Emerging internet and network bank technologies

## Slide 6: The Big Picture

## Slide 7: The Communications Challenge Today
Today’s communications challenge is to create an infrastructure that will deliver information any time, to any place, via any device
Meeting this challenge involves many moving parts and players, and many networks
Constant change is the name of the game
This change occurs in many domains

## Slide 8: Telecommunications Domains

## Slide 9: Regulation
Various forms of regulation exist in telecommunications and networking
Wired and wireless networks in the US fall under federal, state and international jurisdictions, areas covered may include
  Licensing
  Availability
  Reliability
  Customer support
  Technology
  Provider interconnection
  Security

## Slide 10: Guides to IT Regs in Banking
You’re certainly familiar with the FFIEC IT Handbook (I hope!)
  https://ithandbook.ffiec.gov/it-booklets/architecture-infrastructure-and-operations/
It discusses the design of technology, implementation of IT infrastructure, and delivery of services and value:
  Principles and practices for IT and operations as they relate to safety and soundness, consumer financial protection, and compliance.
  Processes for addressing risk in design and implementation of IT systems.
  Principles to help evaluate the delivery of financial products and services.
  Management oversight of AIO and its related components, including governance; common risk management topics; specific activities of AIO; and evolving technologies.

## Slide 11: The Voice Network
The first modern network service!
Telephone network technology has undergone major replacement every 20–30 years
In the past, technology replacement was based on economics driving when replacement took place
Last move was to VoIP, drivers included
  Economics
    Data now more important than voice
    Mobility adds convenience
    Demise of the wireline phone
  Regulation
    Reduced need
  Applications
    Integration with conferencing and IM

## Slide 12: Data Networks
Computer technology has evolved at an unprecedented rate
Businesses first used computers in the 1960s and all communication used private connections of modified voice circuits
Public data networking appeared in the 1970s, but the real change occurred with the commercialization of the internet in the 1990s
Network technology has moved from proprietary to internet-based, even for private networks
The internet continues to change everything
Wireless access has grown in importance

## Slide 13: Video Networks
Video networks started with over-the-air television broadcasts
Many households moved to pay TV to access more content
Technology has moved viewing from “live” to “when convenient” and from the TV to a wide variety of devices
Increasing drive to internet distribution
  Traditional players trying to figure out their roles
  Content owners exploring new distribution models
  Streaming services fighting for eyeballs
  TVs have had to become smarter
Business video
  Was expensive and required specialized equipment
  Now we have many affordable options on the desktop

## Slide 14: Technology
Innovation has played a critical role in telecommunications and networking
Standards also play a significant role
Together they drive new capabilities and interoperability
Historically security was an afterthought – no longer!
Security is an integral part of new products and services
What would our world be like if other technologies had advanced at the same rate? How fast would cars be? What would be the travel time from NYC to London?

## Slide 15: Who are the Major Players in Telecom?
Your table will be assigned a domain in telecommunications. Create a list of 3-5 players in your assigned domain.
  Regulators – who regulates telecom and/or the internet?
  Internet – is it a service, a network, or what? Who runs it?
  Voice – this could be a trick question...
  Video – another trick question? Or is video “special”?
  Technology – who builds telecom / IT stuff?
  Who else is in the mix here?

## Slide 16: Let me ask you…
What are the three most important technology advances in banks this century?
Maybe a better question is “what are the big changes in bank networks since you began your career?”

## Slide 17: Models and Layers

## Slide 18: The Language of Networking
Networking is complex
We have developed approaches to describe and build networks, these include
  Protocols
  Network models
  Layers
Together these concepts provide the basis for the networkers’ lexicon
Familiarity will help in your conversations with a bank’s network team

## Slide 19: Protocols
To communicate, we must have agreements
  Example: Don’t interrupt
  Example: Speak English
  Example: Say, “Please”
Agreements that facilitate communication are called protocols
The study of communications is the study of protocols
The study of data communications is the study of data and network protocols
The complete set of protocols used in a particular network environment is known as a protocol suite

## Slide 20: Models
A hypothetical description of a complex entity or process
  Identifies the major elements and their relationship to one another
  Does not provide implementation details
  An architecture
Model of a home
  Walls, roof, floors, doorways, windows, types of room
  Does not include specific materials, design, construction
Networking model is about the functions that must be present in a network and their relationship to one another

## Slide 21: Layering
Layering breaks a big problem into smaller pieces
Large number of protocols required for interoperability between two applications
Break protocols into subsets, each of which addresses specific, closely related issues
Each layer
  Provides a well-defined set of services to the layers above it
  Receives services from the layer below it
  Knows the set of services that are provided to it
  Does not know how those services are provided

## Slide 22: Two Models Drive Modern Networks
OSI Reference Model
  Original networking model work began in the 1970s
  Standardized by ISO in the 1980s
  Seven-layer model designed for interoperability
  Source for much of the networking terminology
Internet Protocol Suite
  Framework created for data communications networks
  Evolved from work spurred by DARPA and the ARPANET
  The Internet Protocol and Transmission Control Protocol were the foundation of the Suite
  With the broad adoption of the internet the Internet Protocol Suite has become the core protocols used in today’s networks
Familiarity with both models essential for understanding the terminology of networking

## Slide 23: Understanding the OSI RM Layers
Where They Live
End-to-End Layers
(End Systems)
Chained Layers
(All Systems)
What They Do
Interoperability
(Meaningful Work)
Connectivity (Successful Exchange)

## Slide 24: A Closer Look at the Layers
Physical
Bit transmission (distance, speed, medium)
Data Link
Node-to-node correctness (access, bit errors)
Network
Routing (addressing, congestion control)
Transport
End-to-end correctness (sequencing, loss)
Session
Dialogue/session control (logon, checkpointing)
Presentation
Information syntax (compression, encryption)
Application
Information Semantics (email, Web, voice)

## Slide 25: OSI Provides a Reference Framework
Physical
Data Link
Network
Transport
Session
Presentation
Application
Gives us a language to talk about data network technologies
Physical
Data Link
Network
Transport
Session
Presentation
Application
Physical
Data Link
Network
Physical
Data Link

## Slide 26: The TCP/IP Network View
Network Interface
Network Interface
Internet
Application Services
Transport
Network Interface
Internet
Application Services
Transport
Network Interface
Internet

## Slide 27: Bringing the Models Together
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application Services
Transport
Network Interface
Internet

## Slide 28: Let me ask you…
Have you ever heard a bank network team refer to any of the layers in either model?
If so, what layer and what was the context?

## Slide 29: Telecommunications Terminology
IT use the OSI model and TCP/IP as short cuts to describe network elements
Common use include
  Layer 1 – Physical (wired and wireless)
  Layer 2 – Data Link (Ethernet combines L1 and L2 elements)
  Layer 3 – Network (IP)
  Layer 4 – Transport (TCP/UDP)
  Layer 7 – Application Services (HTTPS, SMTP etc.)
Familiarity will help you understand a techie discussion and join the club!

## Slide 30: Application Walkthrough
Let’s look at an application we use everyday: Email
Things we need
  An application like Outlook
    Proprietary application
      Composition/editing
      Viewer
      Repository
      Filtering
    Standard communication protocols
      Email format
      Communications to/from the post office

## Slide 31
Simple Mail Transfer Protocol
  Email format
    Header
    Addressing
    Body
    Attachments
  Connection to server
    Usually to corporate server
    Server may provide additional functions
  Server to server communications
Receiving emails from corporate server
  Commonly use POP or IMAP
Communication path to server
Email
Client
Email
Server
SMTP
POP or IMAP
Email
Server
Email
Server
SMTP
SMTP

## Slide 32
Transmission Control Protocol
  Manages connection to the destination server
    Addressing
    Data transfer
    Receipt acknowledgement
    Disconnects from the server
Messages need to get to the destination server
Email
Server
Email
Server
SMTP
Sender
Receiver
TCP

## Slide 33
Internet Protocol
  Used to move packets between to the destination server
  Implemented in routers that are the gateways between networks
  Packet format
    Header
    Addressing
Routing protocols used to determine how router forward packets
First step is to get to get to the router
Intermediate
Networks
Email
Server
Email
Server
SMTP
Sender
Receiver
TCP
Router
Router
IP
IP

## Slide 34
Ethernet
  LAN connecting devices in a network as defined by the IP address
  To leave the network data needs to cross the LAN (link) to the exit (router/gateway)
  Defines
    Addressing
    Frame format
    Error detection
    Physical connection
SMTP
TCP
IP
Ethernet
IP
Ethernet
Client or Server
Router

## Slide 35
LAN physical connection
  Cabling
  Connectors
  Signal format

## Slide 36: Observations
Breaking down the act of communications into steps simplifies implementation and understanding
Functionality for a specific step may be replaced by a new approach without impacting the other steps
Lots of addressing!
Implemented in different places
  Application – format (SMTP)
  Operating system – connection and routing (TCP/IP)
  Hardware – link (Ethernet)

## Slide 37: The Physical Layer

## Slide 38: Physical Layer
Provides transmission of information between devices
Many forms of connection are available to choose from
Coaxial
Cable
Twisted
Pair
Wireless
Optical
Fiber

## Slide 39: Analog and Digital
Information is classified as analog or digital
Analog information can take on an infinite number of values in a continuum
Digital can assume only a discrete (limited) set of values

## Slide 40: Bits
Binary digit (bit)
A bit is a single number that has only two values: one (1) and zero (0)
The native language of transistor-based computing systems
A bit can also take on any meaning that is two-state
  Yes, no
  True, false
  On, off
Data communications is about transmission of bits between two systems
Old analog systems have moved to digitization of data
  Voice in phone calls
  Music
  Video in TV and streaming

## Slide 41: Modulation
Modulate means “to change or manipulate”
In telecommunications, modulation is the act of making changes in a transmitted signal so that it conveys information
Simple examples include
  Traffic lights
    Steady red means stop
    Blinking red means stop—then you can go
  Dial tone (it’s a landline thing)
    Dial tone tells you the phone is ready for use
    Stutter dial-tone (the dial tone has been modulated) tells you that you have voice mail (and the phone is ready for use)
  Back-up horn on a truck
    The regular beep tells people the truck is backing up
    Speeding up the beep (the beep is being modulated) tells the driver how close he/she is to an object (and tells people the truck is backing up)

## Slide 42: Analog vs. Digital: Signaling
Signaling is analog if the signal transmitted can take on any value in a continuum
  Analog information can be sent directly as an analog signal
  Digital information is transmitted by modulating an analog “carrier”
    Device is called a modem
Signaling is digital if the signal transmitted can take on only discrete states
  Analog information must be approximated by a digital information stream for transmission
    Device is called a codec
  Digital information can be sent directly

## Slide 43: Let me ask you to…
Identify examples of common analog and digital transmission systems
Provide analog information we store and transmit in digital form

## Slide 44: Transmission Rate
Transmission rate is the amount of data per second
Based on three factors
  Bandwidth of the channel
    Channel: A communication path
    Passband: Range of frequencies in a channel
    Bandwidth: Number of frequencies in a channel
  Impairments on the channel
    Noise: Random impairments
    Distortion: Fixed impairments
  Signaling method used
    Analog: Frequency modulation (FM), amplitude modulation (AM)
    Digital: AMI, B8ZS, Manchester, 4B/5B
Measured in bits (or Bytes) per second (i.e., bps or Bps)

## Slide 45: Multiplexing
A technique to share communications capacity
Various methods in use
  Frequency division multiplexing (radio/TV)
  Time division multiplexing (programming/PSTN)
  Wavelength division multiplexing (optical transport)
  Code division multiplexing (cellular networks)

## Slide 46: Media
In modern networks, information is transmitted as
  Electrical energy (copper)
  Light (optics, wireless)
  Electromagnetic energy (wireless)
The medium provides an infrastructure for the transmission of information
The nature of the medium dictates its transmission characteristics
  Attenuation
  Susceptibility to transmission impairments
  Carrying capacity

## Slide 47: Media Options
Electrical
Optical
Radio Frequency
Optical
Wired
Wireless
Single Mode Fiber
Multi- Mode Fiber
Twisted Pair
Coaxial Cable
Carrier- Based
Spread Spectrum
Media

## Slide 48: The Data Link Layer

## Slide 49: Data Link Layer
Connects devices on a shared link
Data is sent in a frame
Common topologies are:
  Point-to-Point
  Any-to-Any
Examples
  Point-to-Point Protocol
  Ethernet
  DOCSIS

## Slide 50: Common Link Topologies
Any-to-Any
internet
Point-to-Point
Access
Data Link Functions
Framing
Addressing
Error check

## Slide 51: Point-to-Point Protocol (PPP)
Commonly found on leased (private) lines and dial-access
Features
  Framing (synchronization, data delimiting, transparency)
  Additional capabilities
    Authentication
    Compression
    IP address configuration
    Multilink operation (MLPPP required) enables multiple channels to carry single data streams (inverse multiplexing)
internet
PPP

## Slide 52: Cellular (Mobile) Networks
Many similarities to Wi-Fi
  Specific bands allocated for the service
  Multiple generations of the technology with each improving performance
  Bands vary by country
  Current generations have added new bands to increase capacity
  Frequency (channel in Wi-Fi) reuse provides coverage in a wide area
Some differences
  Original application was voice, data added over time
  Handoff between cells creates WAN
  Protocols to interconnect carrier networks part of the standards
  Spectrum used requires a license

## Slide 53: Cellular Network Evolution
Analog to digital
Voice to data
Single frequency band to multiple bands (varies by country)
Multiple technology standards globally to one
Increased use of fixed wireless access (FWA) for residential and business internet access
Move to edge computing to support low latency applications (industrial controls and self-driving cars being examples)

## Slide 54: Banking Networks
Private
Network
HQ/datacenter
internet
Branches
WFH
Customers
Service
Providers

## Slide 55: Inside the Branch
What devices do we have in the branch?
How are they used in supporting operations?
What applications do they access and where are they located?
How are they connected?

## Slide 56: Ethernet
Ethernet is the wired LAN technology of choice
Standards created by the IEEE 802 Committee
Equivalent to the Physical and Data Link Layers of the OSI model and the Network Interface in the Internet Protocol Suite
A variety of Physical Layer options meet a wide variety of application needs
  Coaxial cable
  Twisted pair
  Optical fiber

## Slide 57: Ethernet Evolution
1973
1980
2001
Ethernet LAN
Invented
MEF WAN
Standards
IEEE 802.3 LAN
Standards
Hub
Switch
1973 to early 1980s
1980s
1990s to present day

## Slide 58: Some Popular Ethernet Physical Layers
Standard | Length | Cable
10BASE-T | 100 m | Cat 3, 4, 5 UTP
100BASE-TX | 100 m | Cat 5 UTP
1000BASE-SX | 2000 m | MMF
1000BASE-LX | 3000 m | SMF
1000BASE-T | 100 m | Cat 5e, 6, 7 UTP

## Slide 59: Typical Ethernet LAN
Most devices use a standard Ethernet chipset and use twisted pair connections
Autosensing selects speed between 10, 100 and 1000 Mbps
Connections go from the desk to a patch panel or switch
  Allows different speeds on its ports
  Provides the ability to have older devices in the same LAN as newer ones, such an old laser printer that only supports 100 Mbps
Switches can be interconnected
  Twisted pair if close and on the same floor
  Optical fiber used when further apart or on different floors

## Slide 60: Structured Cabling
Which cabling job is better?
What might the cabling say about the IT team?
What do you see in the banks?

## Slide 61: Ethernet Frame
Ethernet LANs allow any device on the LAN to talk to any other device on the LAN (any-to-any)
Addresses are needed to identify who the information is for
Ethernet frames include an address (referred to as the MAC address)
MAC address is assigned by device manufacturer

## Slide 62: Let me ask you…
Do all the devices in the branch need to be able to see one another?
Should we create multiple zones (LANs) to separate devices/functions?

## Slide 63: Multiple LAN Configuration
Allows traffic segmentation, for example data and voice
Simplest way to create multiple LANs (networks) is to have separate physical networks, requires
  Multiple cable drops to the desk
  Switches for each LAN
  Separate inter-switch (trunk) connections for each LAN
Note each LAN (network) will have its own block of IP addresses assigned to it, more on this later
What if we could use one infrastructure and create multiple logical LANs to create separate segments?

## Slide 64: Virtual LANs (VLANs)
VLAN 1
Personnel
VLAN 2
Engineering
Switch
E
F
G
H
A
C
D
Separates End Systems
B
From B Þ All
From B Þ E
From B Þ All
From B Þ E
From B Þ All
From B Þ All
From B Þ All
From B Þ All
From B Þ All
From B Þ All
From B Þ All
From B Þ All
From B Þ All

## Slide 65: VLANs
Logically creates multiple LANs within a switch
Tags used between switches to identify which LAN the frame belongs to
Configured on the switches
Change requires software update versus physical connection change for separate switches
Centralizes switch management

## Slide 66: Let me ask you…
Where might you see VLANs used in a bank?
How do VLANs make an examiner’s life easier or harder?

## Slide 67: Wi-Fi
As ubiquitous as Ethernet in the LAN now
Part of IEEE 802.x family of LAN standards
802.11 is the IEEE name, but we just say Wi-Fi
The Wi-Fi Alliance is helping keep things simple
Theoretical speeds run to multi-gigabits, but the reality is usually slower
Huge variations in experience and management between vendors
Ethernet frame with Wi-Fi extras

## Slide 68: Wi-Fi Standards

## Slide 69: Bands and Channels - 2.4 Ghz

## Slide 70: 2.4 GHz Channel Reuse

## Slide 71: Service Set Identifier (SSID)
Sometimes referred to as a network name in Wi-Fi
Clients connect to a specific SSID
Multiple SSIDs may exist in Wi-Fi channel
  Used to create multiple logical networks
    FDIC CU and FDIC Guest being good examples
AP broadcasts name so devices can join
Like VLAN concept with client required to join
Sometimes an SSID may not be broadcast to hide the network

## Slide 72: 802.11 Security Issues
Unbounded nature of the medium
  Need for encryption and authentication
Original goal to be “equivalent” to wired LAN
  Service set identifiers (broadcast by access point)
  Wired equivalent privacy (WEP)
    Turned off by default
    No user authentication (MAC address only)
WEP problems
  64-bit RC4 encryption
    24-bit known initialization vector (IV) plus 40-bit secret key
    RC4 itself considered relatively weak
  No key distribution system
    All nodes share same key
  No longer supported

## Slide 73: Wi-Fi Protected Access (WPA3)
Ratified by Wi-Fi Alliance January 2018 as a replacement for WPA2
Based on a subset of IEEE 802.11i
Designed for use with an IEEE 802.1X authentication server
Different 192-bit key distribution to each user
Temporal Key Integrity Protocol (TKIP)
  Dynamically changes keys as the system is used
Improved payload integrity
Stronger, safer
Many APs still support WPA2 along with WPA3

## Slide 74: Some Wi-Fi Words: What do they Mean?
Typical specs for a new Wi-Fi device might be:
Wi-Fi 6E certified
2x2/4x4/2x2 MIMO
2.4 Ghz 20, 40 Mhz channels
5 Ghz 20, 40, 80 Mhz channels
6 Ghz 20, 40, 80, 160 Mhz channels
UltraMeshSM technology
WPA2/WPA3
Maximum speeds based on channel width are:
150 Mbps at 20 Mhz
300 Mbps at 40 Mhz
600 Mbps at 80 Mhz
1.2 Gbps at 160 Mhz

## Slide 75: Let me ask you…
How do banks use Wi-Fi?
What risks are associated with Wi-Fi?

## Slide 76: Now We Have LANs
LANs provide links between devices within a network
What makes the network a network?
  Common link
  Assigned block of network addresses (IP)
Connecting to devices (applications) outside of the network needs a gateway (router) between networks
Connections within the same network need a way to identify the LAN address of the destination
IP and associated protocols create networks and ways to interconnect them

## Slide 77: The Internet Protocol
The Network Layer (Layer 3) protocol used on the internet
  Has become the protocol for most networks
  Primary responsibility is building routing tables, forwarding and delivering packets
Current version is IPv4 with IPv6 growing
  Packet-oriented
  Connectionless
Related protocols include
  Routing protocols (RIP, OSPF, EIGRP, BGP)
  Address Resolution Protocol (ARP)
  Dynamic Host Configuration Protocol (DHCP)
  Network address translation (NAT)

## Slide 78: The IPv4 Address
Binary (base two) representation:
    01000111 00111100 10011000 10100000
Better known as:
    71.60.152.160
Hierarchical structure
Like your phone number (area code, phone number)
IP address has the Network Identifier (NETID) and Host Identifier (HOSTID)
Slash notation indicates where the boundary between the NETID and HOSTID is located
128.67.38.23 /16

## Slide 79: Role of IP Addressing
IP addresses are used to identify the client computer and the server
All packets have a destination address (where it is going) and a source address (the sender’s address)
IP addresses
  Assigned to devices
    Static: Permanently assigned to a device
    Dynamic: Temporarily allocated to a device
  Public
    Unique and valid over the Internet
  Private
    May not be sent over the Internet
    Translated by network address translation (NAT) for internet transit

## Slide 80: Static vs. Dynamic IP Address
An IP address can be assigned to a system statically or dynamically
Static assignment is fixed and permanent
  Does not change when a system reboots
  Ideal for inbound communication
    Web servers
    Email servers
    FTP servers
    DNS servers
    VPN access appliances
    Routers
Dynamic assignment means assignment occurs when a system boots
  May change over time
  Ideal for outbound communication (e.g., Web, email)
  Makes it hard for others to find your IP (not linked to DNS)
Dynamic Host Configuration Protocol (DHCP) typically used to assign both static and dynamic IP addresses

## Slide 81: IP Address Allocation
Public addresses are managed by the Internet Assigned Number Authority (IANA)
  Addresses allocated by geographic region
  Regional Registries assign to Internet Service Providers (ISP) and large businesses
Private IP blocks allow businesses to allocate addresses internally without regard to the public addresses
  Network Address Translation (NAT) at the edge converts from private addresses to public addresses

## Slide 82: Private vs. Public IP Address
To overcome address exhaustion private address are used
  10.0.0.0 /8
  172.16.0.0 /12
  192.168.0.0 /16
Private IP address not to be used on the Internet
  Must use NAT/PAT to a public address obtained from ISP
Private
internet
10.1.1.1
blog.hill.com
66.228.126.195
192.168.1.1
192.168.1.2
200.1.1.1
NAT

## Slide 83: IP Address Assignment Example
Access Point
DHCP
NAT
DHCP
DHCP
static
static
static
static
dynamic
dynamic
dynamic
static
static
Rest of the World
Network 1
Network 2
Network 3
Public
192.168.0.0/24
192.168.20.0/24
192.168.10.0/24

## Slide 84: IP Addressing Concerns
Explosive growth of the internet created serious concerns about the depletion of the IP address space
In the 1990s several initiatives were taken to ensure we would not run out of addresses
  Classless inter-domain routing (CIDR)
  Network address translation
  Greater use of private IP address space
  IPv6
Today exhaustion of IPv4 address space is
almost here at the Regional Registries

## Slide 85: Crisis, What Crisis?
IPv4 address exhaustion at IANA occurred in February 2011
Large IP address blocks are no longer available for allocation from the major registries
IP addresses can now be traded
We can get more aggressive address reclamation using NAT
What happens when no more IPv4 addresses are available?

## Slide 86: IPv6: What Is It?
The next generation of IP motivated by the anticipated exhaustions of IP addresses
Developed in the 1990s
New packet header structure (not very backwards- compatible with IPv4)
Expanded address range, 128 bits!
Improved security
Flow definition
Auto configuration built in
Anycast
Significant effort required to migrate

## Slide 87: When Is IPv6 Coming?
It has been around since mid 1990s
Adoption is slow in some areas
More rapid in others
  Areas of the globe with limited IPv4 addresses for their needs
  Mobile phones
  Single purpose devices needing lots of IP addresses (cable boxes)
All major internet connected devices support both IPv4 and IPv6
Overtime more traffic will move over to IPv6

## Slide 88: Routing and Forwarding
These are what routers do to make the internet work.
  Forwarding packets from the source to the destination.
  Building tables of destination networks and the neighbors who can get them one “hop” closer to them. This is called Routing.
Forwarding based on the routing table
Forwarding decision is local
The routing table is maintained by the routing protocol
Routing protocol uses non-local data to build the table
Router can contain rules that determine behavior

## Slide 89: IP Routing
Router 1
Router 2
Network B
Network A
The forwarding of IP packets to the destination
End-to-end path is not predetermined
  Hop-by-hop routing
  Router selects next router based on destination address
Often described as best-effort service
To Network A
Net
Address
Next Hop
.
Network A
Network B
.
.
Router 1
Router 2
.
To Network A

## Slide 90: Following a Packet
TRL
HDR
Packet
Packet
HDR
TRL
Packet
Packet
Packet
Net
Address
Next
Hop
.
Network A
Network B
.
.
Router 1
Router 2
.

## Slide 91: Where Next?
Private
Network
HQ/datacenter
internet
Branches
WFH
Customers
Service
Providers

## Slide 92: Connecting to the WAN

## Slide 93: Bank Branch Connection
Branches need to access applications
  Internal applications at the datacenter
  Core applications at a service provider
  Cloud applications at a cloud datacenter
Common network architecture uses private network connection to the internal datacenter for all traffic
We have a variety of options for the connection
  Private Line
  MPLS
  Carrier Ethernet
  VPN

## Slide 94: Private Lines
Dedicated physical connection or bandwidth between sites or as access to carrier service
Old school technology, such as T1, were originally designed for the public voice network
Most private connections today are optical fiber Ethernet connections to other services
  MPLS
  Carrier Ethernet
Carriers are investing heavily in expanding their fiber footprint
Private wireless networks are an option in come cases

## Slide 95: Ethernet Access
Ethernet has expanded from the LAN to the WAN
Optical fiber is the medium of choice
Dedicated fibers frequently used for business services
  MPLS
  Carrier Ethernet
  Internet access
Shared access offers lower cost option based on Passive Optical Networking (PON) technology
  Originally used for home services
  Cost effective approach for business internet access

## Slide 96: Dedicated Access
Speeds up to 100 Gbps available
Strong SLAs
WAN Service Provider
Dedicated Fiber Pair
Fiber
Termination

## Slide 97: Shared Access
Speeds up to 1 Gbps available
internet Service Provider
Single Fiber
Fiber
Termination
Fiber
Termination
Fiber
Termination
Fiber
Distribution
Up to 32
splits

## Slide 98: Digital Subscriber Line
Internet access using telephone lines
Digital Subscriber Line (DSL)
  Umbrella for a variety of technologies using phone line
  Speeds vary with distance (loop length)
    Typical maximum speeds are 100 Mbps down and 20 Mbps up
    Maximum distance is ~12,000 ft
  Often service of last resort especially in rural areas

## Slide 99: Cable Modem
Cable company data infrastructure
Hybrid Fiber Coax (HFC)
  Fiber from cable company headend to a node (near customer)
  Coaxial cable from node to customers (shared access)
DOCSIS protocols control access and transmission format
  Service speeds available vary based on technology deployed
  Asymmetric speeds often 1.2 Gbps down and 35 Mbps up
  Multi-gigabit symmetric services starting to be deployed
Node
Cable
Modem
Coax
Fiber Pair
CMTS
internet

## Slide 100: Let me ask you…
What is your broadband connection?
If you have options, why made you make this choice?

## Slide 101: Private WANS

## Slide 102: MultiProtocol Label Switching
MPLS provides a private IP network between sites
Introduced in the late 1990s it became the predominant private networking solution
It does not use the internet
Connections to the MPLS service use a variety of private lines
Available everywhere
Carrier Ethernet started to displace MPLS in mid-00’s for higher speed applications
Recently SD WAN has started to become the service of choice for branch networks

## Slide 103: Class of Service
Applications have differing performance requirements
Class of service can be used to prioritize applications with sensitive need
Destination x
Priority normal
Destination x
Priority high
Sorter

## Slide 104: MPLS
MPLS edge functions as a router in the private network
Packets forwarded through the MPLS network to the appropriate edge router
Inherently secure
Provides ability to prioritize packets
Rapid reconfigurations in case of link failure
MPLS
HQ/datacenter

## Slide 105: MPLS Operation

## Slide 106: Carrier Ethernet
Carrier networks have become fiber rich
Growth of fiber in metro areas enabled widespread access to services using Ethernet
Led to industry development of Carrier Ethernet service specifications through the Metropolitan Ethernet Forum (MEF)
Certification of carriers, equipment and professionals has helped interoperability and grown the market
Very popular in metro areas where fiber is widely available

## Slide 107: Carrier Ethernet Connectivity Models

## Slide 108: Use Cases
Point-to-Point
Data replication between datacenters
Connection to partner
  Service provider
  Cloud services
Internet access
Point-to-Multipoint
Secure connection to customers
  Hospital to specialty providers or another hospital system
School district connections from schools to datacenter
Any-to-Any
General connectivity between sites
WAN functions like a big LAN switch
Customers usually put routers on the edge of their network

## Slide 109: The Internet

## Slide 110: Let me ask you…
How has the internet changed banking?

## Slide 111: The Internet
From bulletin boards to…
Businesses use the internet in many ways
  Provide product information to customers
  As a sales platform
  Deliver product support
  Communicate with partners
  Access applications
  Collect and sell user data
  Research
What else?

## Slide 112: The Internet: A Global, Public, Packet Network
Service
Providers
Service
Providers
Internet
ISP
ISP
ISP
ISP
ISP
ISP
ISP
ISP
ISP
ISP

## Slide 113: Connecting to the Internet
A wide variety of access options already discussed
  DSL
  Cable Modem
  Ethernet
Wireless options have increasingly grown in access share
  Mobile phones
  Fixed wireless access
    Mobile
    Wi-Fi
    Satellite

## Slide 114: Cellular (Mobile) Networks
Many similarities to Wi-Fi
  Specific bands allocated for the service
  Multiple generations of the technology with each improving performance
  Bands vary by country
  Current generations have added new bands to increase capacity
  Frequency (channel in Wi-Fi) reuse provides coverage in a wide area
Some differences
  Original application was voice, data added over time
  Handoff between cells creates WAN
  Protocols to interconnect carrier networks part of the standards
  Spectrum requires a license

## Slide 115: Cellular Network Evolution
Analog to digital
Voice to data
Single frequency band to multiple bands (varies by country)
Multiple technology standards globally to one
Increased use of fixed wireless access (FWA) for residential and business internet access
Move to edge computing to support low latency applications (industrial controls and self-driving cars being examples)

## Slide 116: Cellular Concept
Frequency reuse between base stations
Base station to base station handoff
Base station connection to voice and internet at Mobile Switching Center

## Slide 117: 5G
The current generation of cellular wireless
  Still in early stages of deployment
  Lots of variations globally
Key changes from 4G
  New modulation schemes
  More frequency bands
  Higher speeds
  Lower latency
  Fixed wireless options
  Internet of Things (IoT) support

## Slide 118: Back to the Bank
How can the bank
use the internet?
Private
Network
HQ/datacenter
internet
Branches
WFH
Customers
Service
Providers

## Slide 119: Work From Home
VPN offers a secure connection to the bank, cloud and service providers
Encrypted tunnel to VPN server coupled with multifactor authentication
Where should the VPN server be?
  On premises
  In the cloud
Is there anything else we could do for the home network?
  Separate SSID or Access Point
  Corporate owned and managed home-based firewall

## Slide 120: Site-to-Site VPN
Offers low-cost approach to building a WAN
Point-to-Point VPN configured at network edges
VPNs over
the internet
HQ/datacenter
Branches

## Slide 121: VPN as a WAN Challenges
Historically a manual configuration in edge devices
  Potential for errors
  Unlikely to change keys frequently due to effort required
Limited visibility into performance
No control of applications

## Slide 122: Software Defined WAN
SD WAN modernizes the approach to deploying a VPN WAN
PORTAL
Configuration management
Network visibility
Business continuity rules
Security policies
HQ
Datacenter
Branch #1
Branch #2
Control
Data
VPN
SD WAN
CPE
SD WAN
CPE
SD WAN
CPE

## Slide 123: SD WAN
Central configuration and orchestration automates deployment
Greater visibility than traditional WAN solutions
Application-level routing and management
Simple deployment of BCP rules
Often sold as a managed or co-managed solution
Security at the branch level or in the cloud
Secure cloud connectivity
Various implementation models

## Slide 124: Sample SD WAN Implementation
Application Routing
VPN
Security
Performance
Data Gathering
BCP Rules
internet
ISP 1
ISP 2

## Slide 125: Observations for SD WAN Branch Networks
Benefits
  Simpler configuration and implementation
    Connectivity
    Security
    Business continuity
  Greater visibility
    Overall performance
    Application specifics
  Lower cost
  Cloud integration

## Slide 126: Connecting to Servers and Applications

## Slide 127: Transport Layer Connections
Connects client to server
Internet Protocol Suite offers two options
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)
Network
Client
Server
Transport Protocols

## Slide 128: Other Transport Layer Functions
Connectionless and connection-oriented operation
Error detection
  Bit errors
  Packet loss
  Out-of-sequence delivery
Error correction
  Bit errors
  Packet loss
  Out-of-sequence delivery
Application addressing
Flow control
Enhanced capabilities
  Security
  Timing

## Slide 129: Two Options
TCP
End-to-end application connection
Establish connection
Manage connection
Guaranteed delivery and sequence of data
Application addressing
UDP
Connectionless (datagram) communications
Error detection at receiver
Application addressing

## Slide 130: Connectionless Communication
Data Transfer
Stuff

## Slide 131: Connection-Oriented Communication
Can we talk?
Sure!
Stuff
Got it!
I’m Done
K thx bye!
Connection Establishment
Connection Release
Data Transfer

## Slide 132: Let me ask you…
What are connectionless and connection-oriented protocols good for? Do we need both kinds?

## Slide 133: Error Detection and Correction
Bit errors
Packet loss
Out-of-sequence delivery

## Slide 134: Application Addressing
Layer 3 address gets us here
Layer 4 address gets us here…
…or here

## Slide 135: Servers and Listening Ports
Requests for multiple services to a single server
Each request initiates a transport session
The server listens for a request on a specific port to know which application to activate
SMTP Request
HTTP Request
FTP Request
Passive Listening
on Multiple Ports

## Slide 136: Well-Known TCP/UDP Ports
Port identifies higher layer protocol

## Slide 137: Enhanced Functionality
Security
  Typically associated with TCP
  Protocol can implement an encryption capability
  Protocol can implement an authentication capability
  Transport Layer Security (TLS)
Timing
  Typically associated with UDP
  Critical for applications containing time-sensitive information
    Voice applications
    Video applications
  Real-Time Transport Protocol (RTP)

## Slide 138: Sockets
130.1.1.0:80 refers to the Web server at this IP address
Socket = IP address + port number

## Slide 139: Transport Layer Security
Provides secure encrypted connection between client and server
Replaced Secure Socket Layer (SSL) although the terminology of SSL continues to be used
Part of HTTPS (port 443) for secure web traffic
Combines authentication and encryption
Current version 1.3
Some systems may still use v1.2

## Slide 140: Cryptography
The science of writing in secret codes
  Dates back to 1900 BC in Egypt (nonstandard hieroglyphics); probably appeared spontaneously soon after writing was developed
Necessary in telecommunications when communicating over any untrusted medium or storing sensitive information
Three types
  Hash functions
  Secret key
  Public key

## Slide 141: Hash Functions
No key
  Plaintext is not recoverable from the ciphertext
  Examples: MD2, MD4, MD5, SHA-1, SHA-256
  Also called message digests or one-way encryption
Primary uses: digital signatures and password storage

## Slide 142: Secret Key Cryptography
Single key
  Same key is used for encryption and decryption
  Examples: DES, Triple-DES, IDEA, RC4, RC5, AES
  Also called symmetric cryptography
Primary use: Privacy

## Slide 143: Advanced Encryption Standard (AES)
Symmetric key cypher with key sizes of 128, 192, and 256 bits
Block substitution-permutation cypher based on 128-bit block
Number of cycles based on key size
Each cycle performs multiple block substitutions, permutations, and mixing to encrypt the data
ation of the algorithm

## Slide 144: Public Key Cryptography
Two keys based on the prime factors of a large number
  One key is used for encryption and the other for decryption
  Examples: RSA, Diffie-Hellman
  Also called asymmetric cryptography
VPN functions
  Identity verification
  Secret key exchange

## Slide 145: RSA
Diffie-Hellman started the path to public key cryptography
RSA was the first approach to public key systems
Developed at MIT in 1977
Based on creating a public key from the product of two large prime numbers
Key length today is 2048 bits
Used in certificates
Being replaced by Elliptic-curve cryptography using 256-bit keys

## Slide 146: Sample Application: Email

## Slide 147: Final Comments on Cryptography
Cryptography alone cannot guarantee 100% security
But we can achieve a high level of risk acceptance where benefits outweigh the losses
The goal is to balance the possible with the acceptable
Strong cryptographic systems can withstand attacks up to a point
The mathematics is rarely the weak link!
Must consider the threat, system design, implementation, users, and legal/political environment

## Slide 148: Real-Time Transport Protocol (RTP)
A connection-oriented service building on UDP
  Connections are negotiated by other protocols (e.g., RTCP or SIP)
Adds several functions to UDP
  Sequencing
  Packet dependency
  Delay
  Jitter
Commonly used for
  Voice over IP (VoIP)
  IP telephony (IPT)
  IP television (IPTV)
  Any audio/video application

## Slide 149: Port Address Translation
Transport Layer header information allows multiple internal hosts to share the same public IP address
PAT works closely with NAT
200.1.1.1:5478
200.1.1.1:6748
192.168.1.30:5478
192.168.1.20:5478

## Slide 150: Application Services

## Slide 151: It’s All About The Applications
Applications perform tasks to deliver services to users
Communications is the act of users interacting with software performing the desired function
Application services define the protocols for communication and services supporting communication
Two models exist
  Client-server
  Peer-to-peer

## Slide 152: Application Layer Concerns
Information syntax
Information semantics
  What the information means
    What information elements are required
    How the information elements are exchanged
Applications types
  User applications
  Network support facilities
  Resource sharing utilities
  Network management packages

## Slide 153: Clients and Servers
Client
Server
That system’s got something I need…
I’ve got something that system wants…
Network
Desktops
Laptops
Tablets
Cell phones

## Slide 154: Service Relationship: Client/Server
Applications have clearly defined roles
  Client initiates request
  Server responds to client’s request
Server software is passive but available
  Connects to local Transport Layer and waits for connection requests
Client transient in nature
  Application is enabled on-demand
  Connection to local Transport Layer is made/broken as needed
Examples
  HyperText Transfer Protocol (HTTP)
  Simple Mail Transfer Protocol (SMTP)
Network
Client
Server
Application
Protocols

## Slide 155: Service Relationship: Structured Peer-to-Peer
Unstructured peer-to-peer is difficult to coordinate
  How do you find the peers?
  Many support the concept of seeds or “super peers”
Structured peer-to-peer combines client/server with unstructured peer-to-peer model
  Servers used for search, discovery, coordination
  Peers used to do the actual work
Examples
  BitTorrent
  Instant messaging (IM)

## Slide 156: Let me ask you…
What application communications model is used in banking?

## Slide 157: How Do We find Applications?
The Domain Name System (DNS) provides a distributed directory of internet resources
Essentially the directory assistance of the internet
Converts uniform resource locators (URLs) to IP addresses
Registries are databases that contain the domain names under the top-level domains they administer
Registrars are accredited companies that delegate domain names to interested parties

## Slide 158: Domain Name System Exposed
Range of information in DNS Databases
A records
PTR records
MX records
CNAME records
TXT records
Local DNS
I know MyCompany.com
TLD DNS Servers
We know who to ask
What is Outside.com’s
IP address?
Who can I ask?
Ask the DNS server at this IP address
What is Outside.com’s IP address?
Answer
Answer
We know OtherCompanies.com, etc.
Other Local DNS
Great now I can contact them
I would like to get Outside.com

## Slide 159: Email Services
Your_Name@aDomain.TLD

## Slide 160: Let me ask you…
Is Google Gmail an email service, a WWW service or something else?

## Slide 161: Simple Mail Transfer Protocol
Client/server model
Simple, text-based command language
  Identify sender and receiver(s), transmit message, and provide confirmation
Developed to transport simple text notes only
  Extended using MIME to include attachments
Requires retrieval protocols
  Post Office Protocol v3 (POP3)
  Internet Message Access Protocol (IMAP)
  HyperText Transfer Protocol (HTTP) for web-based access
Sending Client
Intended Recipient
Sender’s Server
Recipient’s Server
SMTP
SMTP
POP3, IMAP

## Slide 162: Summary
Data communications is described using a mix of models
Breaking functions into manageable chunks simplifies understanding
Functions are implemented in a combination of areas
  Hardware
  Operating systems software
  Application software
New applications frequently reuse existing code which can add existing, but often unknown, vulnerabilities in the new application
Security has moved from an add-on to a build-in necessity

## Slide 163: Network Diagram Review
Review attendee provided network diagram or use previously shared network diagram

## Slide 164: Voice Networks

## Slide 165: Thoughts on Telephony
It changed the world
Ability to talk in real time over long distances changed society
  News could be learned in real time
  Commerce could be conducted quickly
  Relationships made and maintained
Spurred technology innovation
  AT&T Bell Labs was a global leader in invention and development
  AT&T competition was equally inventive
Was the home of tech giants in its heyday
Telephone networks were used to connect computers
Now relegated to being an application in a world of data

## Slide 167: Telephone Network Elements
Trunk

## Slide 169: North American Numbering Plan
10-digit structure of telephone numbers in North America
Three components
  Numbering Plan Area (NPA) or area code
    Uses NXX numbering structure (675 useable codes)
    Assigned on geographic basis
    Do not cross LATA boundaries
  Exchange or central office (CO) code
    Uses NXX numbering structure (792 usable codes)
    Assigned to central offices/exchanges
  Line number
    Identifies particular line/station attached to a particular switch
802
655
0940

## Slide 170: Private Branch Exchange
PBX places telephone switch on business site
  CapEx reduces OpEx
Phones connect to switch using premises wiring
Switch connects to the PSTN using a trunk
Offered lots of features
Very popular 1980s to early 2000s
Many business have migrated to hosted solutions

## Slide 171: Voice moves to IP
The 1990s saw the commercialization of the internet
As the internet took off, millions of users were looking for things to do in this new world
Innovation drove significant advances in technology of networking, computing and applications
As corporate networks moved to IP technology, so did the world of telephony
Voice over IP (VoIP) has almost completely replaced the old phones and switching systems
VoIP may, or may not, use the internet for connection and transport

## Slide 172: VoIP Brings New Capabilities
Greater call control capabilities managed via a portal
Allows simple call forwarding to other devices (phones, apps)
  One number, many devices, anywhere
Mobile phone apps allow calling from the office number within the app
Rich in traditional telephony features, simpler to use
Integration with conferencing capabilities (video, chat/IM, etc.)
Improved business continuity options

## Slide 173: Let me ask you…
How many of you have landlines?
What percentage of business calls do you do via Teams (or equivalent)?
How do banks use desk phones?

## Slide 174: IP Phone Options
Conventional Telephone
Voice
Gateway
IP Phone
Softphone
IP Packet Network

## Slide 175: Signaling Control: The Role of SIP
Signaling protocol for multimedia sessions
Dominant IPT signaling protocol
IP Phone
Signaling Control
SIP

## Slide 176: SIP Trunks
An IP telephony (IPT) trunk
Designed for use with an IP PBX
Typically shares voice and data
  Burst data when voice not in use
  Maximum concurrent calls configured
Call signaling over the trunk is SIP
Private Corporate IP Network
Carrier Voice Services
IP Network
SIP Trunk

## Slide 177: Hosted VoIP
Back to the old model of the intelligence (switch) being in a provider’s network
Offers many business continuity capabilities
Generally lower cost than premises solution for small and medium sized businesses
Like old systems most features are lightly used
Solutions may use the internet for access or private (trunk) connection

## Slide 178: VoIP Network Considerations
Does the VoIP traffic share a LAN with data?
How is voice quality ensured?
What type of connection is used to connect to the PSTN?
If this connection goes down, what happens to the ability to make and receive calls?
Do employees have portal access to manage their phone service? If so, what access controls are in place for them?
What bank functions may be impaired by the loss of telephone services?

## Slide 179: Voice System Review
Review attendee provided telephone
network diagram

## Slide 180: Network Security

## Slide 181: Networks
Private
Network
HQ/datacenter
internet
Branches
WFH
Customers
Service
Providers
Where are the threats to security in this diagram?
What questions do we need to ask?

## Slide 182: Network Security
It starts with taking inventory
  End user systems
  Servers
  Network elements
  Networks
Followed by risk analysis
Activities and tools designed to protect the usability, reliability, integrity of a network and corporate data housed within.

## Slide 183: Inventory
If we don’t know we have it, we can’t protect it
End user systems and servers contain networking elements that need to be kept current (patched)
Many systems are now being networked and are classified as part of the Internet of Things (IoT)
Networking elements and networks need to be protected and require attention beyond those supporting end user systems
Technology refresh needs to be part of the plan

## Slide 184: Internet of Things: Some Sample Things
Automation
Communication
Monitoring
Transportation
Management
Intelligence?

## Slide 185: IoT Security Concerns
Estimates for IoT suggest 20 billion devices will be connect via the internet in the next 10 years
What emphasis will be placed by developers on security?
Will consumers and businesses implement controls?

## Slide 186: IoT Things to Consider
What mechanism is used to track the devices?
How are updates made to the device?
Can the device be checked by the vulnerability scanner?
What data is collected by the device and where is it stored?
What software is on the device? Can it be hardened?
How are the devices configured and managed? Can access be recorded in the log system?
What connectivity options are there for the device? How are they managed?

## Slide 187: Ethernet Considerations
Switch location and access
Administrative access control
  Limit who has access
  Log access and changes
  Closely manage remote access
Firmware and management software patching
Rogue device identification
VLAN design, management, interconnectivity
Encryption

## Slide 188: Wi-Fi Considerations
Access Points should be commercial grade
Firmware upgrade
Control access to resources through the creation of separate networks (SSIDs) based on need
Use strong passwords
  Change policy
Rogue devices
Management access controls
Implement time profiles to stop after hour access
Mesh management

## Slide 189: WAN Considerations
Management access controls and logging
Provider and customer roles
Access
Business continuity
Private
  SLAs
  Encryption
  Zone implementation
Internet
  Perimeter protection (firewall, IDS/IPS…)
  VPN management
    Certificates, AAA...
    Licenses
Private Line
Ethernet
MPLS
internet

## Slide 190: Voice Security Considerations
Management access and controls
Patching
Separate LAN zone
Encryption
On premises or hosted
Connection to provider
  Private
  Internet
Business continuity

## Slide 191: Many Sources for Baseline Security Measures
NIST Cybersecurity Framework
Council on Cybersecurity Critical Security Controls
ISO 27001/2
International Information Systems Security Certification Consortium (ISC2)
Vendor whitepapers and case studies

## Slide 192: Service Provider Security Solutions

## Slide 193: Managed Security Solutions
Security has become a critical infrastructure issue
Threats growing more complex and sophisticated
Skilled security personnel shortages drive outsourcing
Outsourcing some or all of security a growing industry
Usually called Managed Security Service Providers

## Slide 194: Many Players
Network equipment manufacturers
  Moved to offer security in their offerings
  Security capabilities include subscription for capabilities and ongoing monitoring, updates and management portal access
Security software and equipment providers
  Historically limited focused offerings
  Many expanded service set or have been acquired
    Broader range of security offerings (e.g. perimeter security added endpoint)
    With AI and ML, monitoring has become integral to the product
    Expansion into network space
    Professional services (design and incident response)

## Slide 195: Some More Players
Computer manufacturers
  Extension of their professional services business
  SOC services
Telecommunications service providers
  Networks need protecting security often an integral part of the service
  Expansion into professional services
Systems integrators
  Natural expansion of their professional service offerings
Local IT providers
Financial service technology providers

## Slide 196: Emerging Technologies

## Slide 197: Software Eats the World
Marc Andreesen (Netscape, Andreesen Horowitz)
Every device, appliance or box in this course is going away or being consolidated with others
They are being replaced with software running on:
  General purpose silicon (CPUs)
  Graphics processors (GPUs)
  Embedded Devices
  Almost everything else (IoT, appliances, smart devices)
This trend is not confined to networking!

## Slide 198: Virtualization
Virtualization started with the recognition that server power had increased significantly and most servers were underutilized
Servers often support a single application only
The 1960’s virtual machine concept came to the rescue
One server can now act as multiple virtual servers
Concept has expanded to storage and networks
Application
Operating
System
Hardware

## Slide 199: Virtual Machines Benefits
Application
Operating System
Virtual Machine
Application
Operating System
Virtual Machine
Application
Operating System
Virtual Machine
Virtual Infrastructure
Servers
Storage
Storage
Network
Network

## Slide 200: Cloud Deployment Models
Cloud services come in four variants
  Private – infrastructure deployed for a single entity
  Community – provisioned for a community (e.g. government agencies)
  Public – open to use by anyone
  Hybrid – combination of two or more cloud infrastructures
Many organizations use cloud services for select applications
Multi-cloud is the norm
Migration ongoing for most organizations
Responsibilities depend on deployment and service model

## Slide 201: Cloud Service Models
Facility, power, rack, environment controls, fire control
Hardware
Hardware
Hypervisor
Hypervisor
OS
OS
Application
Application
Access Controls
Provider
Customer
Responsibility
Colo
IaaS
PaaS
SaaS

## Slide 202: A Step Beyond Virtualization
Clouds initially took existing applications and placed them on virtual servers
Each virtual server has its own full-blown operating system
Containerization looks at separate (isolated) application space
  Operating System (OS)
  Application
Multiple application containers may run in the same OS container (virtualized OS)
OS container may offer limited functions (lightweight) reducing processor load
Automated orchestration to manage cloud workloads (e.g. Kubernetes)

## Slide 203: Traditional Application Approach
Application a single entity with multiple functions built-in
Developed using a single programming language
Large complex code set
Difficult to modify and redeploy
If one function is busy a whole new instance needs to be turned up to meet the demand
Monolithic
Application
User
Interface
Browse
Function
Shopping
Cart
Payment
User
Profile
Product
Database

## Slide 204: Containers and Microservices
Cloud infrastructure offers offers a highly scalable environment for computing, storage and communication across multiple datacenters
Containers along with automated orchestration offer a flexible, scalable computing environment
Microservices implement functions independently in their own container
Microservices communicate with one another to deliver business services
User
Interface
Browse
Function
Shopping
Cart
Product
Database
User
Profile
Payment

## Slide 205: Microservices
Independent processes
Processes connect via APIs and send data through a communications or messaging system
If one process is loaded a new instance of that microservice can be spun up
Benefits
  Independent development (small teams, different languages...)
  Easier to update
  Scalable
  Expandable
Many support tools to facilitate orchestration, communication, workload assignment, security, deploy updated services…

## Slide 206: Not just Much Cheaper, the cloud is Much Better.
Performance, Business Continuity, and Disaster Recovery are all improved by a cloud approach.
  Geographic diversity, fate-sharing, availability risk of all kinds is well-addressed in the hyperscale clouds.
  Things better centralized, like compliance, become much easier with a single point of access.
The advantages are worth the risks (to most.)
  Security is still a concern, but being addressed by advances in e.g. authentication and encryption.
  More comprehensive, better correlated customer data can improve outcomes for banks and customers.
These benefits come with a new reliance on the network.
Which is why telecom and data communications are such important topics for banks and regulators.
21st Century bank IT To-dos:
Build new data center.
Buy and deploy new servers.
Acquire offside DR location.
Reinvent the wheel. Again.
Take an application-focused approach.
Support innovation for the bank.
Access the same tools as the big guys.
Use data to remain competitive.
Lower expenses, owned>hybrid>public.
Improve and secure network access.

## Slide 207: The Changing IT Landscape
Businesses are undergoing a digital transformation
New applications increase knowledge and efficiency
Applications are migrating to the cloud
Networks need
  Increased bandwidth
  Simplified management
  Greater visibility
These all improve in a cloud context!

## Slide 208: Bank Network Topics

## Slide 209: Core Processing in the Cloud
Historically, Core Processing was owned by a handful of specialized companies
Moving to the cloud poses both advantages and risks for core processors
Fintech solutions can rapidly add new capabilities and change what “core” means
Will the cloud come to the core before the core comes to the cloud?

## Slide 210: Let me ask you…
What types of applications should banks move to the cloud first?
List some advantages and disadvantages of cloud services from a security perspective.

## Slide 211: Network Talent and Trust as Risks
As network service become more powerful, they become more complex
Management software and AI should make things easier
But understanding and trusting solutions is still important
What happens if the one person at the bank who understands the network quits?
What happens if the bank can’t trust an outsourcing provider?
Education
Certification
Standards
Cross-training
Knowledge in Depth
Outside opinions
What else?

## Slide 212: Community Bank Innovation
Small banks are conservative followers, right?
  They better not be, or they will lose!
Many big bank tools are available to all banks
  Big Data
  Artificial Intelligence / Machine Learning
  Modern tools + personal service
The speed and capability of these depend on the network

## Slide 213: M&A
Small banks often get bought, or merge with other small banks
  Networks have made this inevitable
When companies come together, their networks come together too
Connections must be made between
  Systems
  Devices
  Networks
  Policies
  Services

## Slide 214: Fintech
Not just for the big banks any more
Innovation available to everyone in many areas
  Payments - Apple Pay, Google Pay, and many other Pays
    How much do banks lose to Square, PayPal and Venmo?
  Microsoft Cloud for Financial Services and other clouds
  Blockchain – bitcoin and other cryptocurrencies
  Crowdfunding – Patreon, Kickstarter, Gofundme
  Insurance – disruptive companies and new policies
As these compete, they seek to partner
Cloud platforms and APIs make partnering easy
  Even small banks can get in on the action

## Slide 215: Thank You!
Matt Kolon
matt@hillvt.com
(802) 899-0704